Input File Format (.claw)

Each beat is one note – for some tab this is half notes because it’s in 2/4. The beats are the number of notes in a bar.

Descriptor	Description
&	Blank note
xxxffff	xxx are string skips. ffff are frets. If any of the new frettings change the current fretting then the whole fretting is overwritten.
(chord)	This places “chord” on the top line, and the chord definition in the same format is xxxffff taken from key chord_”chord”
!	Add a brush using the current fretting.
Pf Hf /f	Modify the last note to be a pull off, hammer on or slide to f.

Frets (0-17)	0 1 2 3 4 5 6 7 8 9 n l w t u f s v

OutputFile Format (.plux)

A music line (1 bar per line) begins with a ‘|’. Empty bar lines are ignored. There are 8 notes in a bar irrespective of the beats.

Bar line data is :

1-5	select string
a-z	set fretting and pluck that string this note
+	add hammer on 1 (multiple)
-	sub pull off 1 (multiple)
/	slide 1 (multiple)
=	Change the width of the slide from 2 notes to 1 note.
.	go to next note.
(Chord)	set display chord

The + - / modifiers mean the fretting specifies the start position. So 2/4 would be 2//.

An information list begins with a ‘.’ and has the format .<name> := <value> (no spaces)

Supported information items are : (default values in brackets)

beats	default beats per bar (4)
tempo	default beats per minute play speed (80)
step	amount tempo increases every play when on speed-up (4)
tuning	current tuning. Supports gcgcd and (gdgbd)

others are ignored.

Lines beginning with // are comments and ignored.

Different Display Usage

Minimising the interface for different displays.

float Interface(command as integer,bar ref as bar,dispInfo ref as dispInfo,params as IFParams)

Initialise
Load Resources for the display.

Create
(param 1 : bars in tune)

Draw background, set up for specific tune (if full page tab display sizes for example)
Create empty display information records for each bar which are all non-displayed

Destroy

Remove background
(Hide all display resources is done by the caller)

Visible
(bar,param 1 : position in music in bars float)

Returns non-zero if the given bar is partially displayed at that music position.

Show
(bar,param 1 : position in music in bars float)

Move the bar at a given position, creating if necessary, modifying if necessary.

Hide
if drawn , Free up all the bars display resources.

ID allocation (10000 onwards)

+0...+19	Note#1	0..4 note specific 5x3 for each displayed note.
+20..+39	Note#2
+40..+59	Note#3
+140..+159	Note#8
+160..+199	Reserved	Allocated for general use.